## Slide 1
Touchdown Point
Inference from ADS-B
Fleet-wide landing-overrun risk monitoring, built from the data every aircraft already broadcasts.
Where the wheels touched · how fast · how sure we are
Notes: This project measures where each landing touched down and how fast, using only the surveillance data (ADS-B) that every airliner already broadcasts — with an honest, calibrated confidence attached to every estimate. It exists so overrun-risk monitoring can cover essentially all landings instead of only the recorder-equipped subset.

## Slide 2
The problem
Runway overruns are a leading serious-accident category — and today their precursors are measured on a fraction of flights.
Two measurable precursors — touching down too far along the runway, and touching down too fast. Both eat into the pavement left for stopping.
Today's measurement — requires onboard recorder (QAR) downloads — available for a minority of operations, unevenly across fleets and operators.
The consequence — most landings are invisible to overrun-risk analysis; the near-misses worth learning from go unexamined.
Landings measurable for overrun risk today
Recorder-equipped & shared (filled) vs. unmeasured (hollow) — illustrative proportions
Notes: Runway excursions are consistently among the top categories of serious commercial accidents. The two measurable precursors are long touchdowns and fast touchdowns. Today those can only be measured on flights whose recorder (QAR) data is available and shared — a minority, unevenly distributed. The dot grid is illustrative, not a measured fraction.

## Slide 3
The opportunity
The data already exists — every airliner broadcasts its position and speed, and it's recorded fleet-wide.
4–5 s
ADS-B broadcast interval
Position, speed, altitude — for essentially every flight.
$0
New collection cost
Already recorded at scale.
The idea — if touchdown can be inferred from ADS-B, overrun-risk monitoring extends from the recorder-equipped subset to essentially all landings.
The catch — touchdown is never directly reported in ADS-B — it has to be reconstructed from the trajectory.
The answer key — 40,500 flights with matched recorder data give ground truth to calibrate against and to grade every accuracy claim.
Notes: ADS-B is broadcast by every airliner about every 4-5 seconds and recorded fleet-wide — no new collection needed. If touchdown can be inferred from it, risk monitoring covers essentially all landings. Touchdown isn't in the data directly; we reconstruct it, and we can grade ourselves because 40,500 flights have matched recorder ground truth.

## Slide 4
Why it's hard
The data was built for air-traffic awareness, not for pinpointing touchdown.
touchdown: between reports
ADS-B reports every 4–5 s
≈ 900 ft between consecutive reports
About three football fields at landing speed — touchdown almost never falls on a report.
late & variable the on-ground flag
It flips after real touchdown — a sanity bound, never the answer.
2 clocks position vs. speed timestamps
Merging them naïvely injects up to ~430 ft of error — as large as the answer itself.
Notes: Three pathologies: (1) at landing speed the aircraft covers ~900 ft between reports and touchdown always falls between two of them; (2) the aircraft's own on-ground flag transitions late and inconsistently, so it can only bound the answer; (3) position and speed messages carry different timestamps — merging them naively injects an error (~130 m at approach speed) comparable to what we're measuring.

## Slide 5
The approach
Estimate the time of touchdown to sub-second precision, then map time to a runway position.
Physics
Deceleration knee, descent-curve crossing, tracking filter — interpretable, explainable to regulators.
Change-point
Statistical detection of the instant the motion switches from flying to rolling.
Learned
Models trained on 40,500 recorder-matched landings — the expected accuracy leader.
Calibrated fusion — blends all methods, down-weighting whichever look unreliable on each specific landing
Output: touchdown point (ft from threshold), touchdown speed — each with a calibrated confidence interval
Notes: Every method estimates the *time* of touchdown to sub-second precision; position follows by interpolating the trajectory at that time and projecting onto the runway. Seven estimators across three families run on each landing; a calibrated fusion combines them, down-weighting methods that look unreliable for that specific flight. Different methods fail on different landings — the ensemble is what controls the long-landing tail that drives overrun risk.

## Slide 6
Why to trust it
Designed for a safety case, not just accuracy: graded, calibrated, explainable, and honest about failure.
40,500
flights of ground truth
Every method is graded against recorder data, with leakage-controlled train/test splits (no aircraft appears on both sides).
90% ≈ 90%
calibrated confidence
Intervals are recalibrated on held-out data so stated confidence matches reality — verified, not assumed.
2 answers
every estimate is explainable
Each machine-learned estimate ships with an interpretable physics estimate beside it, for regulators and analysts.
0 guesses
fails loudly, never silently
When data is insufficient the system says “no estimate” with a machine-readable reason — it never fabricates an answer.
Notes: Four trust pillars: (1) 40,500 recorder-matched flights as an answer key, with leakage-controlled splits so no airframe appears in both training and test; (2) confidence intervals conformally recalibrated so 90% empirically means ~90%; (3) an interpretable physics estimate accompanies every learned estimate; (4) insufficient data yields an explicit 'no estimate' with a reason code — a confident wrong answer is the most dangerous output a safety system can produce.

## Slide 7
Status & next step
Built and tested end-to-end — the remaining step is empirical.
460
automated tests passing
Full pipeline: ingestion, quality gates, estimators, fusion, calibrated uncertainty, validation harness.
7
estimation methods fused
Physics, change-point, and learned families — with per-landing reliability weighting.
250 ft
provisional accuracy target
RMSE on touchdown point — held provisional until real-data runs ratify it.
Next: run the 40,500-flight corpus → measure the accuracy floor set by the 4–5 s data cadence → ratify the targets
The decision this enables: continuous, fleet-wide monitoring of landing-overrun risk across all operations — not just the recorder-equipped subset — with statistically honest per-landing confidence.
Notes: The system is code-complete with a 460-test suite covering 23 formal correctness properties. Accuracy targets are deliberately provisional: the next step is running the recorder-matched corpus to characterize the error floor imposed by the 4-5 s reporting cadence, then ratifying the 250 ft RMSE target. The payoff is overrun-risk monitoring across all operations with honest per-landing confidence.